## Slide 1: Nerd Herd 687 Programming Curriculum
Programming a Flywheel

## Slide 2: General overview
Setup command-based
  Make OI, RobotMap, and Robot if they aren’t already there
  Make folders for subsystems, commands, and constants
Make subsystem for flywheel
  Create the subsystem’s class and put a motor controller in it
  Put a few methods to apply voltage/speed to the motor
  Create the subsystem in Robot.java
Make a simple command for spinning the flywheel
  Create the command’s class
  Make the command apply a voltage to the flywheel in execute()
  Add the command in OI

## Slide 3: Setting up Command-based

## Slide 4: Creating a subsystem
Make a new file called <SubsystemName>.java, using PascalCase for the name
  Subsystem name should describe the system it controls (e.g. “Arm”, “Drive”, “Shooter”, etc.)
Make a class in that file, with correct package and such, that extends Subsystem (have to import Subsystem from wpilib)
Make constructor and initialize motor controller in it
Add abstract inherited method (initDefaultCommand())
Add a method to apply voltage to motor with <talonName>.set(ControlMode.PercentOutput, <voltage>)

## Slide 5: Example Subsystem Code

## Slide 6: Creating a Simple Command (1)
In the commands folder, create a new file, <CommandName>.java, with Pascal-case because naming conventions
  Command name should be an action with an associated subsystem (e.g. “SetFlywheelVoltage”, “SetArmPosition”, “DriveForward”, etc.)
In constructor, initialize any variables necessary (voltage to set)
In initialize(), do any necessary things (nothing for flywheel)
In execute(), perform necessary actions (set the voltage of the motor for a flywheel)
In isFinished(), perform a check to see whether the command should finish (we won’t do anything beyond return true for now here)

## Slide 7: Creating a Simple Command (2)
In end(), prepare your system for new commands (set flywheel voltage to 0)
In OI, add a Joystick object (named <something>stick, or something of the sort)
In OI, add a JoystickButton object, and initialize it with the Joystick already created and the button number
  Naming conventions for JoystickButtons: <functionOfButton>_<buttonNumber> Ex: driveForward_3 for driving forward with button 3
Run the method <joystickButtonName>.whenPressed(new <CommandName>) to make the button run the command when pressed

## Slide 8: Example Simple Command